## Slide 1: Smoothing your data with polynomial fitting: a signal processing perspective
Cees Taal

## Slide 2: About me (Cees Taal)
Academia:
  PhD, TU Delft, speech signal processing (2008-2012)
  Postdoc, KTH, Stockholm, speech enhancement (2013)
  Postdoc, LUMC, Leiden, Cochlear implants (2014)
Industry:
  Philips Research, biomedical signal processing (2014-2016)
  Toon, IoT data processing/analysis (2016-now)

## Slide 3: I have to confess…
8 years of Matlab
  Pretty standard in signal proc.
Python since last year
  Best decision ever :)
  Pycharm IDE
MatlabPython? Just ask me!

## Slide 4: Motivation
A signal processing perspective?
  Savitzy-Golay filtering
  Frequency domain interpretation
  Not today’s topic: Optimal noise removal
Electrical Engineering
Computer Science
Signal Processing
Remove noise from your data
  With polynomial fitting

## Slide 5: Polynomial fitting
Given a set of data points:
Polynomial fit:
p = np.polyfit(x, y, deg=m)
y_fit = np.polyval(p, x)

## Slide 6: Polynomial fitting - smoothing
In the real world we have noise:
Use fit to estimate clean data:

## Slide 7: Polynomial fitting - windowing
Difficult to fit long time-varying signals:
  Need high polynomial degree
  Numerical errors
Alternative approach:
  Fit in short-time windows
  Better fit with low degree
(10th degree fit)

## Slide 8: Polynomial fitting - windowing
Procedure:
  Extract short-time window
  Fit polynomial to window
  Evaluate polynomial
    e.g. at center of the window
  Repeat for shifted window
y_fit = polyfit_window(y, window_length, deg)

## Slide 9: Polynomial fitting - windowing
Example:
  3rd degree polynomial
  100s window
  Polynomial evaluated at 50s

## Slide 10: Polynomial fitting - windowing
Difficult to see effect of free parameters:
  Window size, polynomial degree etc.
The Savitzky-Golay (SG) filter*
  Equals polynomial smoother, differently implemented
  Facilitates frequency domain interpretation
  Gives better interpretation of free parameters
*Savitzky, Abraham, and Marcel JE Golay. "Smoothing and differentiation of data by simplified least squares procedures." Analytical chemistry 36.8 (1964): 1627-1639.

## Slide 11: A Signal Processing Perspective
https://xkcd.com/26/
Before frequency analysis of SG-filters we need some background:
  Fourier transform
  Linear time-invariance
  Convolution theorem

## Slide 12: Fourier transform
Fourier transform decomposes signal into sum of sinusoidal components:
Fourier transform
Inverse Fourier transform
X = np.fft.fft(x)
x = np.fft.ifft(X)

## Slide 13: Linear Time Invariance
Polynomial smoothing is a linear time-invariant system (LTI)*
  (We need this property later)
Linearity
Time Invariance:
  *Schafer, Ronald W. "What is a Savitzky-Golay filter?" IEEE Signal processing magazine 28.4 (2011): 111-117.

## Slide 14: Linear Time Invariance
Any LTI-system can be fully described by its impulse response
import scipy.signal as sig
sig.convolve(x, h)
Any LTI-system can be applied by a convolution:

## Slide 15: Linear Time Invariance
SG-filter impulse responses
  Window length of 100 samples
  Polynomial degrees [1, 3, 5, 7]
import scipy.signal as sig
h = sig.savgol_coeffs(window_length=101, polyorder=m)

## Slide 16: Convolution Theorem
Time-domain convolution equals frequency-domain multiplication
Time-domain
Frequency-domain
(85 samples, 8th degree)
Input
SG Impulse R.
Output

## Slide 17: SG-Filter Frequency Response
Effect of polynomial degree
  Window-length is 15 samples
  Low-pass effect
  Higher degree increases cutoff freq.
  Little effect on slope

## Slide 18: SG-Filter Frequency Response
Effect of window length N
  Polynomial degree is 6
  Also low-pass effect
  Higher length decreases cutoff freq.
  Little effect on slope

## Slide 19: Back to the real world
Application: Electricity monitoring in the Toon
Meter module:

## Slide 20: Toon Electricity Monitoring
LED
Sensor
Electricity meter
(topview)
Reflected light
Time
Pulse-interval measures
electricity consumption

## Slide 21: Toon Electricity Monitoring
What if you just turn off the LED?
  Pulse not visible, few bits, quantization noise

## Slide 22: Toon Electricity Monitoring
Let’s have a look in the frequency domain
Pulse
Quantization noise
Ambient light

## Slide 23: Toon Electricity Monitoring
And back to the time domain!

## Slide 24: To conclude
Polynomial filtering:
  Is an LTI-system which act as a low-pass filter
  Fourier analysis helps tuning free parameters
Main goal hopefully achieved:
  Get acquainted with Fourier analysis
  (NOT how to optimally remove noise)
https://github.com/chtaal/pydata2017

## Slide 25
Cees Taal
We’re recruiting for a Data Scientist / Machine Learning Engineer!
Like math, signal processing, dirty hand? M.Sc. Thesis projects available!
https://github.com/chtaal/pydata2017